Attachment no 2

ORDER DESCRIPTION

- Object of the contract

The subject of the order is the supply of gas purifier listed below by name and quantity needed:

1.  Gas purifier AsH3 and PH3 with isolation valves 		2 pcs.

- The scope of the subject of the contract

A detailed description of the subject of the contract is provided in section 5 of this document. The total price for the product specified in point 1 should include the total cost along with the packaging and delivery to the headquarters of the Employer.

- Criterion

Offers will be evaluated according to a point scale with a maximum number of points of 100.

| Criterion | Maximum number of points S | Method of awarding points |
| --- | --- | --- |
| Net price (P) | 100 | S x Pmin/Pi |

Where:

- Pi – net price of goods with delivery - for the given offer

- Pmin - the minimum delivery net price for the ordered goods from all offers submitted

- S – number of points

The final score will be calculated by adding up the partial components and then rounded to two decimal places. (rounded from "5" up)

- Deadline for completing the order

As soon as possible, no later than 10 weeks from the date of placing the order.

Deadline for completion of the order includes readiness to hand over the goods to the Ordering Party, which complies with application of the EXW Incoterms2020 principle.

According to the EXW (ex works) principle, the moment of delivery of the goods is considered to be the moment of placing of the goods at the disposal of the buyer at place indicated by the supplier (factory, plant etc.).

The Ordering Party shall accept application of other Incoterms2020 principles (such as FCA, DAP etc.)

- Parameters

| Product name | Parametrer | Specification |
| --- | --- | --- |
| Gas purifier AsH3 and PH3 with isolation valves | Gases purified | AsH3 PH3 |
|  | Impurities | H2O ≤ 1 ppbV O2 ≤ 1 ppbV Metals ≤ 1 ppbV |
|  | Materials of construction | Housing: 316L stainless steel |
|  | Maximum flow rate | ≤ 10 slpm |
|  | Maximum operating pressure – purifier only | ≤ 1,400 psig |
|  | Maximum operating pressure –purifier with options | ≤ 250 psig |
|  | Pressure drop, with 0.0015 μm particle filter | ≤ 1,0 psid |
|  | Isolation valves | Connection size (VCR) - ¼” Inlet/outlet connection type (VCR) - Male/male Outside Diameter - 38,1 mm (1.5”) Overall length (OAL) - 127 mm (5.0”) |